## Slide 1: Design and Development of an IoT-Enabled Health Condition Monitoring Kit
Supervised By:
Prof. Dr. Md. Aminul Haque Akhand
Prof. Dr. Md. Sheikh Sadi
Presented By:
Name: Arpita Das
Roll: 1607067
Name: Shimul Dey Katha
Roll: 1607086
Thesis Defense
Department of Computer Science and Engineering
Khulna University of Engineering and Technology, Khulna-9203, Bangladesh

## Slide 2: Presentation Outline
Introduction
Problem Statement
Objectives
Related Works
Methodology
Experimental Analysis
Conclusions
References

## Slide 3
Introduction

## Slide 4: Problem Statement
Health is a primary concern of every human being. Several life threatening diseases can be easily monitored by IoT enabled health monitoring kit.
Raspberry Pi can be used as an core device for wireless communication and cloud communication.
However, IoT enabled health monitoring system might be an effective solution with less complications.

## Slide 5: Objectives
To develop a continuous health condition monitoring kit.
To monitor the health conditions such as:
1. Body temperature,
2. Heart beat,
3. Movement of the body,
4. Sweat gland activity related to emotional arousal,
5. Blood oxygen level and
6. Blood Pressure.
Admin can see the health condition of the patient from anywhere through the firebase database.

## Slide 6: Related Works
Author | Year | Display Device | Hardware Components | IoT Enabled
Nookhao et al. [2] | 2020 | LCD display and computer | Temperature sensor,heart beat sensor,arduino,WIFI module | Yes
Priya et al. [3] | 2019 | Monitor or smartphone | Body temperature sensor,pulse rate sensor,Raspberry pi | Yes
Tariq et al. [18] | 2019 | Smartphone | Heart beat sensor | No
Table 1: Observation on Existing Systems

## Slide 7
Methodology

## Slide 8: System Overview
The health condition monitoring kit which is proposed mainly developed in two parts:
a)Sensor’s data acquisition.
b)Data analysis, storage and visualization to the cloud.
The system follows three tier architecture.

## Slide 9: System Overview (cont.)
Fig. 1: The flow diagram of the system.
Fig. 2: The data flow of the system.
Layer1
Layer2
Layer3

## Slide 10: Hardware Implementation
Fig. 3: The Schematic Circuit of the System.
Blood Pressure Module
Health Parameter | Sensor
Body Temperature | LM35 sensor
Heartbeat | Pulse sensor
Body motion | adxl345 accelerometer sensor
Sweat glant activity | GSR sensor
Blood oxygen level(SpO2) | MAX30102 pulse oximeter
Blood pressure | Developed by ourself
Table 2: Sensor Equipments.
Serial Communication

## Slide 11: Blood Pressure Module
Fig. 4: Circuit of blood pressure module.
BP module composed of two parts:
Hardware part:
Arduino board,
An air pump,
An air valve,
An inflatable cuff,
A pressure sensor and
An amplifier circuit.
Software Part:
1. Arduino IDE

## Slide 12: Integrated System
Fig. 5: The Circuit of the System.
Heartbeat Module
GSR Module
Accelerometer Module
Temparature Module
SpO2 Module
Blood PressureModule

## Slide 13: Data Upload
Fig. 6: Upload data to firebase cloud database.

## Slide 14
Experimental Analysis

## Slide 15: Performance Analysis
The evaluation of the research to check the performance is done by several experiments.
The health parameter values have been monitored during the working of the project.
The examination of the system is done by several tests.

## Slide 16: Performance Analysis: Body Temperature
The body temperature is measured and compared with the actual tempratature measured using thermometer.
Users | Temperatureusing lm35, F | Temperatureusing thermometer, F | Average accuracy
User1 | 95.4 | 98.4 | 
User2 | 100.3 | 100.6 | 
User3 | 96.3 | 99.0 | 96.19%
User4 | 93.3 | 98.0 | 
User5 | 89.9 | 97.9 | 
Table 3: Comparison between Measured temperature and Actual temperature.
accuracy calculated using equation-

## Slide 17: Performance Analysis: Heartbeat
Users | Heartbeatusing pulse sensor, bpm | Normal heartbeat, bpm | Average accuracy
User1 | 76 | 78 | 
User2 | 79 | 82 | 
User3 | 88 | 89 | 96.77%
User4 | 81 | 84 | 
User5 | 90 | 95 | 
Table 4: Comparison between measured heartbeat and actual heartbeat.
Heartbeat measured in BPM.

## Slide 18: Performance Analysis: Body Motion
Motion of a user in X, Y and Z axes.
 | X axis value | Y axis value | Z axis value
Before motion | -4 | 25 | 213
Before motion | -4 | 25 | 213
After motion | 62 | 13 | 204
After motion | 74 | 12 | 195
Table 5: Accelerometer sensor value of an user.

## Slide 19: Performance Analysis: GSR value
User | GSR data
User1 | 195
User2 | 199
User3 | 201
User4 | 190
User5 | 210
Table 6: GSR sensor values for different users.

## Slide 20: Performance Analysis: SpO2 and Blood pressure
Users | Blood Oxygen Level(%) | Blood Pressure | 
 |  | Systolic | Diastolic
User1 | 95 | 78 | 125
User2 | 96 | 82 | 130
User3 | 95 | 85 | 135
User4 | 97 | 84 | 135
User5 | 96 | 75 | 120
Table 7: SpO2 sensor values and blood pressure values for different users.

## Slide 21: Performance Analysis (cont.)
 | Temparature Sensor | Heartbeat Sensor | Accelerometer Sensor | GSR Sensor | SpO2 Sensor | Blood pressure Module | IoT Enabled
Nookhao et al. [1], 2020 | Yes | Yes | No | No | No | No | Yes
Priya et al. [2], 2019 | Yes | Yes | No | No | No | No | Yes
Tariq et al.[3], 2019 | No | Yes | No | No | No | No | No
Proposed System | Yes | Yes | Yes | Yes | Yes | Yes | Yes
Table 8: Comparison Between Existing Systems and Proposed System

## Slide 22: System Demonstration

## Slide 23
Conclusions

## Slide 24: Concluding Remarks
We designed a system to monitor health parameters of a person and visualized parameter data anywhere anytime using IoT.
The developed system is a user friendly system.
Though many improvement can be made to the system, it can play an important role in health monitoring sector.

## Slide 25: Future Works
More health parameters (EEG,ECG) can be added.
Data storage system with ensuring data security can also be added.

## Slide 26: Publication from the Thesis
Das Arpita, Shimul Dey Katha and Muhammad Sheikh Sadi. "An IoT Enabled Health Monitoring Kit Using Non-Invasive Health Parameters." In 2021 International Conference on Automation, Control and Mechatronics for Industry 4.0 (ACMI), pp. 1-6. IEEE, 2021.
https://doi.org/10.1109/ACMI53878.2021.9528227

## Slide 27: References
[1] Nookhao, S., Thananant, V., Khunkhao, T.: Development of IoT Heartbeat and Body Temperature Monitoring System for Community Health Volunteer. Joint International Conference on Digital Arts, Media and Technology with ECTI Northern Section Conference on Electrical, Electronics, Computer and Telecommunications Engineering (ECTI DAMT NCON). pp. 1–4. (2020)
[2] Priya, A. D., Sundar, S.: Health Monitoring System using IoT. International Conference on Vision Towards Emerging Trends in Communication and Networking (ViTECoN). pp. 1–3. (2019)
[3] T. Tariq, R. M. A. Latif, M. Farhan, A. Abbas and F. Ijaz, "A Smart Heart Beat Analytics System Using Wearable Device," 2nd International Conference on Communication, Computing and Digital systems (C-CODE), pp. 137-142, 2019.

## Slide 28
Thank You